## Slide 1
📡
SOFTWARE DESIGN DESCRIPTION · V3.4
SunMRRC
SunSDR2 DX · Mobile Remote Radio Control
📡 HTTPS / WSS
🎛️ DSP Pipeline
🎤 TX Voice
🛡️ PTT Safety
⚡ Per-band Power
16
SDD Chapters
12
Architecture Decisions
5
WebSocket Endpoints
8
PTT Safety Layers
5
SVG Diagrams
Python 3.12 · FastAPI / Uvicorn · NumPy / SciPy · Web Audio API · vanilla JavaScript · WDSP
Document ID: SDD-SUNMRRC-2026-001 · IBM TeamSD v2.3.2 · https://radio.vlsc.net:8889
01 / 16

## Slide 2
CHAPTER 1
Executive Summary
SunSDR2 DX mobile-first browser remote control — V1.0 production release
📱
Mobile-first PWA
iPhone/Safari primary target · HTTPS/WSS secure context · Touch-optimized · Safe-area support · Service worker · Manifest
🔊
Real-time RX Audio
IQ demodulation (USB/LSB/AM/FM) · Tagged dual-codec (Opus 28kbps / Int16 PCM) · WDSP NR2/AGC · S-meter · Waterfall
🎤
TX Voice Modulation
Web Audio EQ chain (4 presets) · AudioWorklet 48k→16k · Opus encode · Hilbert SSB · tanh soft limiter · DRIVE power control · On-air verified
⚡
Per-band TX Power
Device DRIVE (0x0017) sqrt-taper · /api/band_power + Band Power UI · band_power.json persistence · Re-sent on QSY/PTT
🛡️
PTT Safety System
8-layer defense in depth · ACK retry 3× · Backup s: channel · 30s watchdog · Touch-move-out release · Forced-RX handler
📐
Architecture Record
16 SDD chapters · 12 ADs · 5 SVG diagrams · 16-slide PPTX · TeamSD methodology · Full protocol documentation
02 / 16

## Slide 3
CHAPTERS 2–3
Business Direction · Project Definition
Goals · Objectives · Scope · Success Criteria
🎯 Business Goals & Objectives
G1
Mobile RX Confidence
G2
Safe Remote Control
G3
Minimal Deployment
G4
Design Continuity
G5
Incremental Extensibility
8 Objectives — 6 Implemented · 1 Open (ATR)
5 Strategies — Mobile-first · Direct UDP · Browser audio
6 Tactics — HTTPS default · WSS select · PTT ACK loop
📋 Project Scope
▶ In Scope
• Mobile web UI
• 5 WebSocket endpoints
• RX audio + waterfall
• TX mic → Hilbert SSB → IQ
• Per-band DRIVE power
• /api/band_power + mem_channels
• HTTPS/WSS auto-start
• Direct SunSDR2 DX UDP
• DSP mode + WDSP toggles
• SDD documentation
⊘ Out of Scope
• Native iOS/Android app
• Cloud multi-tenant
• ATR-1000 backend (stub only)
• CW/FT8/Logbook pages
• Hamlib rig abstraction
✅ 9 Success Criteria — All Met
03 / 16

## Slide 4
CHAPTER 4 · APP 011
System Context
Actors · External Interfaces · Data Flows · System Boundaries
📱 Mobile Browser
iOS Safari / Chrome · Web Audio API · WASM Opus Touch UX · PWA Manifest · Service Worker · Canvas
HTTPS/WSS — 5 WebSocket Endpoints
/WSCTRX (control) · /WSaudioRX (RX audio) · /WSaudioTX (TX mic) /WSspectrum (waterfall) · /WSATR1000 (tuner placeholder)
🖥️ FastAPI SunMRRC Server
server.py · Static files · Auth middleware · TLS auto-detect IQ processing loop · TX pacer thread · /api/band_power + mem_channels
imports → web_control/
sunsdr_direct.py (UDP protocol) · dsp.py (IQ DSP + TX modulator) opus_rx.py (server-side Opus) · wdsp_wrapper.py (NR2/AGC)
📡 SunSDR2 DX Hardware
UDP :50001 Control (DRIVE 0x0017 · PTT · Frequency) UDP :50002 IQ Stream (0xFFFE RX · 0xFFFD TX · 0x1F00 Telemetry)
4 Actors: HAM Operator · System Maintainer · Browser Runtime · SunSDR2 DX | 11 External Interfaces | 9 Data Flows
04 / 16

## Slide 5
CHAPTER 5 · ART 0507
Non-Functional Requirements
7 categories · 25 NFRs — Performance · Security · Compatibility · Operability · Audio Quality
⚡ Performance (7 NFRs)
NFR-001 RX audio latency: low enough for live monitoring
NFR-002 Control response <200ms · PING→PONG ms display
NFR-003 Spectrum ~512B/frame @ 38Hz (~19 KB/s)
NFR-004 Audio Opus ~18-24kbps (PCM ~256kbps)
NFR-005 CPU stability: no sustained DSP overload
NFR-006 Client fan-out: multi-browser without crash
NFR-007 Waterfall: adaptive noise floor, smooth render
🔒 Security (4 NFRs)
NFR-020 HTTPS/WSS secure origin for mobile production
NFR-021 TLS key files never embedded in docs/code
NFR-022 HTTP fallback only when certs missing or DISABLE_SSL=1
NFR-023 Auth boundary: no false claim of server-side auth
🎵 Audio Quality (4 NFRs)
NFR-060 RX Int16 PCM → Float32 decode path
NFR-061 USB/LSB/AM/FM/CW demodulation quality
NFR-062 WDSP NR2/NB/ANF/NF/AGC when libwdsp loads
NFR-063 TX: Hilbert SSB + tanh soft limiter, clean envelope
NFR-065 Per-band DRIVE (0x0017) sets TX power
🔧 Operability + Maintainability (6 NFRs)
NFR-040 Logging: startup, TLS, radio connect, IQ bind
NFR-041 Env config: DEVICE_HOST, WEB_PORT, DISABLE_SSL
NFR-042 Certificate expiry monitoring scripts
NFR-043 Service worker bypasses JS/HTML cache
NFR-050 Small backend: handlers understandable in server.py
NFR-051 Explicit gaps: planned hooks documented until removed
05 / 16

## Slide 6
CHAPTER 6 · ART 0508
Use Case Model
4 Actors · 6 Core Use Cases · 6 Extended / Planned Use Cases
UC-001
Start Mobile Session
Open https→login→power on→WS connections→UI live
✅
UC-002
Remote Receive Audio
IQ→decode→demod→Opus/PCM→/WSaudioRX→play
✅
UC-003
Tune Frequency & Mode
setFreq/setMode→radio/DSP→getFreq/getMode ack
✅
UC-004
Monitor Spectrum & S-Meter
FFT→quantize→/WSspectrum→adaptive floor+colour ramp
✅
UC-005
PTT & Tune Control
PTT press→TX→release→ACK retry→backup s:→watchdog
✅
UC-006
Adjust DSP & Audio
WDSP/NR2/NB/AGC/gain/filter→DSP setters→broadcast
✅
UC-007
Browser Mic TX Audio
Mic→EQ→AudioWorklet→Opus→WS→Hilbert SSB→0xFFFD IQ
✅
UC-008
Memory Channel Save/Recall
Menu→edit→POST /api/mem_channels→mem_channels.json
✅
UC-013
Per-band TX Power
Band Power menu→edit drive %→POST /api/band_power→apply
✅
UC-009
ATR-1000 Power/SWR
Website placeholders; /WSATR1000 stub only
⚠
UC-010/11
CW Decoder / FT8 Automation
Menu links removed (pages absent)
✕
UC-012
Recordings
recordings.html + server-side RX MP3 via ffmpeg
✅
06 / 16

## Slide 7
CHAPTER 7 · APP 408
Subject Area Model
7 Subject Areas · 18 Entity Definitions · State Ownership
ClientSession
WS memberships, UI state
Browser cookies/JS
RadioControl
Freq · PTT · Gain · Filter · Tune
Runtime (SunSDR2DXClient)
IQStream
UDP intake → complex samples → DSP feed
In-process (UDP socket)
RXAudioFlow
Demodulation → Opus/PCM → playback
In-process + WS broadcast
SpectrumFlow
FFT · S-meter · Waterfall render state
In-process + WS broadcast
DSPConfig
Mode · WDSP · AGC · Notches · Filters
Runtime + cookie replay
OperationalConfig
Host · Port · TLS · Env vars · Scripts
Filesystem (env, certs, logs)
Key entities: TXModulationFrame · TXDriveConfig · BandPowerConfig · MemoryChannel · WaterfallRenderState · SMeterState · WDSPConfig · TLSConfig
07 / 16

## Slide 8
CHAPTER 8 · ART 0513
Architecture Decisions
12 ADs — Architectural · Design · Performance · Safety · Extensibility
AD-001
FastAPI/Uvicorn
Async server, native WS, small surface
AD-002
Direct UDP Control
Verified SunSDR protocol, no Hamlib
AD-003
DSP-Owned Mode
Hardware mode-agnostic, SW demod selects
AD-004
Tagged Dual-Codec Audio
Opus+PCM RX and TX, 1-byte tag, no race
AD-005
Quantized Spectrum
512 uint8 bytes/frame, compact waterfall
AD-006
HTTPS/WSS Default
iOS secure context, mic+AudioContext require
AD-007
PTT Release Safety
8-layer defense in depth, ACK retry, backup s:
AD-008
Optional WDSP
Falls back cleanly, UI queries availability
AD-009
Gap Tracking
Document hooks until backend exists or removed
AD-010
Device DRIVE Power
0x0017 per-band, sqrt taper byte, re-send QSY
AD-011
0x1F00 Telemetry
off30 f32=W · off16 u16/10=V · off18=°C · NO SWR from device
AD-012
TX Gain Staging
Preamp ×1.5 + drive gain ×3.0 + tanh@1.0 ≈ 4% engagement
08 / 16

## Slide 9
CHAPTER 9 · ART 0512
Architecture Overview
Four-layer stack — Browser → FastAPI server → shared DSP → SunSDR2 DX hardware
📱 Mobile Browser (iOS Safari / Chrome)
controls.js
mobile.js
tx_audio_eq.js
ptt_manager.js
WASM Opus
Web Audio API · AudioWorklet 48k→16k · Canvas waterfall · Touch PTT · PWA / Service Worker
HTTPS / WSS
/WSCTRX · /WSaudioRX · /WSaudioTX /WSspectrum · /WSATR1000 (?token= auth)
🖥️ FastAPI / Uvicorn Server (server.py)
Auth + TLS
IQ Loop
TX Pacer
/api/band_power
/api/mem_channels
Static serving · 5 WS endpoints · client fan-out · IQ decode → DSP feed · adaptive TX pacing (5.12ms/pkt) · 0x1F00 telemetry
in-process import
⚙️ Shared DSP / Protocol (web_control/)
sunsdr_direct
dsp.py
TXModulator
opus_rx
wdsp_wrapper
UDP protocol · SpectrumProcessor (FFT) · AudioDemodulator (SSB/AM/FM) · Hilbert SSB + tanh · server Opus · NR2/AGC
UDP :50001 / :50002
📡 SunSDR2 DX Hardware (192.168.16.200)
Ctrl :50001 (DRIVE 0x0017 · PTT · Freq) · IQ :50002 (0xFFFE RX · 0xFFFD TX · 0x1F00 telem) · PA — no ALC
09 / 16

## Slide 10
CHAPTER 9 · SIGNAL FLOW
Signal Processing — RX + TX Chains
IQ demodulation downlink · Hilbert SSB modulation uplink · gain staging
🔊 RX: IQ → Audio
UDP Intake
24-bit Decode
→
IF Shift +30.5kHz
→
SSB Bandpass
→
5:1 Decimate
→
AGC (WDSP opt)
→
Opus Encode
→
/WSaudioRX Broadcast
→
Browser Playback
→
Waterfall: IQ→FFT(2048,hanning)→dB clip[-120,0]→uint8 quantize 512B→/WSspectrum @~38Hz→⏫ accumulate 10→30th %ile noise floor→blue bias+contrast gain→colour ramp
S-Meter: FFT→90th percentile→S9=9+(p90+73)/6→asymmetric EMA(attack α=0.5,release α=0.15)→stable needle,fast-rise slow-decay
Codec: Server ctypes libopus · bitrate via opus_encode() max_data_bytes cap (avoids arm64 variadic ctl) · Client WASM OpusDecoder · 1-byte tag per frame · Default Opus ~18-24kbps
🎤 TX: Mic → RF (Client + Server)
📱 Client: micSource → preamp(×1.5) → antiAlias(LP 4.5kHz ×2) → eqLow(350Hz pk) → eqMid(1500Hz pk) → eqHigh(2700Hz sh) → midCut → presence → compressor(3:1,thr=-24) → makeup(×1.6) → noiseGate → AudioWorklet(48k→16k Int16) → Opus encode → /WSaudioTX
🖥️ Server: TxOpusDecoder → TXModulator.feed_audio() → fractional resampler(16k→15625Hz) → overlap-save Hilbert SSB(MARGIN=256,80-sample hops) → upsample ×2.5(→39063Hz) → drive gain(×3.0×drive%) → tanh(1.0) soft limiter → 24-bit IQ packing(vectorized numpy) → jitter buffer(prime 24/reprime 12) → TX pacer(5.12ms/pkt,adaptive ±15%) → 0xFFFD UDP :50002
📊 Gain Staging (AD-012): in peak ~0.50 → Hilbert peak ~0.65 → drive gain peak ~1.95 → tanh(1.0) peak ~0.96 (4% reduction)
❌ OLD (preamp ×3.0): in peak=1.00 → Hilbert peak=1.32 → drive gain peak=3.95 → tanh peak=0.999 (75% reduction → HEAVY DISTORTION on every loud syllable)
📡 Device: 0xFFFD @195 pkt/s (39063 Hz IQ) → DRIVE command (0x0017) per-band power → PA (no ALC) → Antenna | ⚡ Tune bypasses entire chain: pre-computed IQ, TX_TUNE_SCALE=0.35 → ~10W safe continuous
🔑 RF power = DEVICE DRIVE only. Client gain = healthy digital level. Server gain = lifts into tanh knee. Turn drive ↑ for more power, not client gain.
10 / 16

## Slide 11
CHAPTERS 10–11
Service & Component Model
12 services · backend / frontend / shared DSP components
🔌 Service Portfolio
StaticUIService
mobile PWA assets from static/
ControlService
/WSCTRX command dispatch + state sync
RXAudioService
IQ→PCM→Opus /WSaudioRX fan-out
TXAudioIngressService
/WSaudioTX mic→TXModulator
SpectrumService
FFT quantize /WSspectrum fan-out
SunSDRDeviceService
UDP protocol, boot, heartbeat
IQProcessingService
receive, decode, feed DSP
DSPService
demodulation + optional WDSP chain
TXPowerService
0x0017 DRIVE per-band + /api/band_power
BandPowerService
per-band drive % JSON persistence
MemoryChannelService
/api/mem_channels JSON persistence
TLSStartupService
cert/key auto-detect, HTTP fallback
🧩 Key Components
Backend (Python)
• FastAPIApp — routes, startup, static serving
• RadioClient — UDP protocol (sunsdr_direct.py)
• IQLoop — UDP socket, packet validation, DSP feed
• TXModulator — Hilbert SSB, drive gain, tanh, IQ pack
• TXPacer — adaptive pacing, jitter buffer
• RxOpusEncoder / TxOpusDecoder — ctypes libopus
• BandPowerAPI / MemChannelAPI — JSON persistence
Frontend (JavaScript)
• controls.js — WS, codec, waterfall, S-meter
• mobile.js — UX, menus, DSP panel, settings
• tx_audio_eq.js — 4 EQ presets, compressor, preamp
• tx_capture_worklet.js — AudioWorklet 48k→16k
• ptt_manager.js — ACK retry, watchdog, state sync
• tx_button.js — touch PTT, lock, warm-up frames
• opus_codec.js — WASM Opus encode/decode (28kbps)
Shared DSP (Python)
• StreamProcessor · SpectrumProcessor · AudioDemodulator · TXModulator · Opus Codec · WDSPWrapper
11 / 16

## Slide 12
CHAPTER 12 · ART 0522
Operational Model
Startup · Configuration · TLS · Connection Matrix · Verification
🚀 Startup & Config
restart.sh → kill old by cwd → clear port → background start.sh → simple foreground launcher restart.sh -f → foreground with live logs DISABLE_SSL=1 → HTTP debug (no iOS mic support) Environment: DEVICE_HOST=192.168.16.200 (default) WEB_PORT=8889 (default), restart.sh uses 8080 WEB_PASSWORD=sunmrrc (override with env) Runtime persistence: band_power.json → per-band drive % (Band Power UI) mem_channels.json → memory channels (/api/mem_channels) server.log → runtime logs (when background-started)
🔐 TLS + Auth
TLS Auto-detection: certs/fullchain.pem + certs/radio.vlsc.net.key Both present → HTTPS/WSS (iOS requires) Missing or DISABLE_SSL=1 → HTTP fallback check_ssl_expiry.sh for cert monitoring Auth (password-based session): /login → POST /api/auth/login → sunmrrc_auth cookie Token lifetime: 30 days (cookie max-age) All routes + WS require ?token= query param _auth_tokens server-side set, invalidated on restart Connection Matrix: Browser ↔ SunMRRC : HTTPS/WSS SunMRRC ↔ SunSDR2 DX : UDP :50001 / :50002 IPs: 192.168.16.100 ← → 192.168.16.200
🔍 Verification Checklist
Verify HTTPS
server.log → "sunmrrc https://..."
Verify Radio
server.log → "SunSDR2DX: True"
Verify RX
UI /WSaudioRX connected, waterfall flowing
Verify Codec
Opus active → bitrate ~18-24kbps
Verify PTT Safety
getPTT:false after release, release ACK confirmed
Verify TX Power
W= in server.log from 0x1F00 off30 f32 forward watts
Verify TX Quality
TX chain lim: peak ~0.96 (not 0.999 → distorted!)
Verify Gain Staging
in peak ~0.5, drv peak ~2.0, lim peak ~0.96 @ 1 Hz
Diagnose Jitter
/tmp/tx_probe.csv + /tmp/tx_rx_probe.csv
Level Probes
TX chain in:/an:/drv:/lim: lines at 1 Hz in server.log
12 / 16

## Slide 13
CHAPTER 13 · ART 0530
Feasibility Assessment & Known Gaps
Production-ready feasibility · open issues · risk matrix
✅ Feasibility: Production Ready
RX Technical
High
IQ→demod→broadcast→playback — implemented
Control
High
All radio + DSP commands implemented
TX Voice
High
Full pipeline: mic→Hilbert SSB→IQ, on-air verified
Mobile
High
HTTPS/WSS solves iOS blocker, all features on phone
Operational
High
Single process, restart script, simple ops
Extensibility
Medium-High
WDSP optional, ATR hook preserved, clean module boundaries
⚠ Open Issues
I3: /WSATR1000 missing — stub only, no real HW interface ATR-1000 is the only SWR source (device has no reverse-power) I5: Fixed LAN IPs (192.168.16.100 / 192.168.16.200) Should move to env/config for deployment flexibility I7: start.sh prints HTTP URL even with TLS present Align script message with server TLS behavior Resolved (2026-06-25/26): I10: TX power formula — now off30 f32 direct float watts I11: TX voice distortion — client preamp 3.0→1.5 I1-I2, I4, I6, I8, I9: all resolved in prior releases
📊 Risk Matrix
R1
iOS HTTP instead of HTTPS
Medium
R2
Fixed LAN IP mismatch
Medium
R3
TX release lost (half-open socket)
Low
R4
WDSP library unavailable
Low
R8
Stale frontend assets
Low
R9
Certificate expiry
Low
R10
PA over-drive (no ALC)
Low
Resolved Risks
R5: TX audio not transmitted ✓ R6: ATR frontend connection errors (mitigated) ✓ R7: Memory channel API missing ✓ I11: TX voice distortion (gain staging) ✓ I10: TX power cubic fit wrong ✓
13 / 16

## Slide 14
CHAPTER 15 · SAFETY
PTT Safety — Defense in Depth
Release is more safety-critical than keying. No single point of failure can trap the radio in TX.
LOCAL
browser-side
1
Touch UX
touchend · move-out
cancel · mouseleave
touchId tracking
tx_button.js
2
State Machine
isProcessing lock
pendingStop queue
3s leak → unlock
tx_button.js
3
Watchdog
30s hard timeout
force-release all
fires even if
event loop frozen
NETWORK
delivery guarantee
4
ACK Retry
setPTT:false → 1s
await getPTT:false
retry 3× echo
ptt_manager.js
5
Backup Channel
wsAudioTX "s:"
independent socket
server forced-RX
separate from ctrl
6
PING Health
5s PING/PONG
timeout → dead
s: + force reconnect
controls.js
FALLBACK
always-RX
7
Page Lifecycle
visibilitychange · blur · pagehide → forcePTTReleaseIfActive()
iOS suspends JS when backgrounded → touchend never delivered · tx_button.js
8
Server Authority
ws_ctrl() s: → radio.set_ptt(False) + dsp_proc.set_ptt(False)
broadcast getPTT:false to ALL clients · always available · server.py
🛡️ GUARANTEE: every failure mode — lost packet · half-open socket · frozen tab · app backgrounded — has an independent path back to RX
14 / 16

## Slide 15
DEEP DIVE · AD-011
Device Telemetry — 0x1F00 Packet Layout
Verified against real 40m drive sweep (expert_40m_drive.pcap) × external wattmeter + ExpertSDR3
34-Byte Packet: 0xFF32 header (10B) + seq + flags + off16(u16) + off18(f32) + off22(f32) + off26(f32) + off30(f32)
Sent continuously in RX and TX modes · Device does NOT expose reverse power → cannot compute SWR → use external ATR-1000 for SWR
✅ off30: f32
Forward Watts
PEP envelope · Direct float Monotonic: 28%→3W 71%→54W 88%→83W 100%→101W No cubic/linear fit needed
✅ off16: u16/10
Supply Volts
~136 (13.6V) at idle Sags as power rises 0W→13.6 50W→13.1 100W→12.9V Correlation with W = -0.79
✅ off18: f32
PA Temp °C
~42°C · Barely moves Monitors PA thermal state during extended TX sessions Frontend: getTXTelem: watts,volts,temp,W_int
⚠ Previously Wrong (corrected 2026-06-25)
off14 u16 + cubic fit
(pwr_raw-9)³×1.91e-5: non-monotonic noise, never tracked power
off16 u16/100 as "SWR"
actually supply voltage — stable when NOT keyed → rules out SWR
off22 f32 as "reverse power"
actually AVERAGE forward power (ratio to off30 ≈ SSB crest factor)
off26 f32 as "SWR alt"
always exactly 1.0000 — device placeholder · 323+ packets identical
Frontend: getTXTelem:watts,volts,temp,W_int → UI displays W · VOLT (replaces former SWR) · TEMP
15 / 16

## Slide 16
SunMRRC
SunSDR2 DX Mobile Remote Radio Control · SDD V3.4
📖 SDD Version Journey
V1.0
2026-03-15
Original MRRC TeamSD document set
V2.0
2026-05-02
MRRC V5.0 mobile UI and capability update
V3.0
2026-06-21
Re-baseline: FastAPI/Uvicorn, SunSDR2 DX direct UDP, explicit gaps
V3.1
2026-06-21
Waterfall rendering + S-meter smoothing
V3.2
2026-06-23
TX voice + DRIVE power + memory channel API documented
V3.3
2026-06-24
Dual-codec audio + SWR field correction + 11 ADs — V1.0 release
V3.4
2026-06-26
Telemetry correction · TX gain staging (AD-012) · 3 new SVG diagrams · PTT Ch 15 · 16 chapters
🔗 Resources
🌐 Live Radio
https://radio.vlsc.net:8889
📖 SDD Docs
https://www.vlsc.net/sunmrrc/sdd/
🔧 GitHub
https://github.com/cheenle/sunsdr
📥 PPTX Download
https://www.vlsc.net/sunmrrc/sdd/SunMRRC-Architecture-SDD-V3.4.pptx
📐 SVG Diagrams
https://www.vlsc.net/sunmrrc/sdd/diagrams/
16
SDD Chapters
12
Architecture Decisions
5
WebSocket Endpoints
8
PTT Safety Layers
5
SVG Diagrams
4
TX EQ Presets
195
TX IQ pkts/sec
~20kbps
Opus Bandwidth
Document ID: SDD-SUNMRRC-2026-001 · 2026-06-26 · Python 3.12 · FastAPI/Uvicorn · NumPy/SciPy · IBM TeamSD v2.3.2 · GPL-3.0
16 / 16